## Slide 1: Definitions
  literal(리터럴, 문자):
    a variable or its complement
    # of literals determines the complexity of an expression
    ab' + bc'd + a'd +e' : 8 literals
  product term
    one or more literals connected by AND
  standard product term or minterm
    a product term that includes all the variables, either complemented or not
    for 4 variables, w, x, y, and z
      w'xyz , wxyz: minterm
      wy'z : not minterm, but product term

## Slide 2
  sum of products(SOP)
    one or more product terms connected by OR
    ex)
      w'xyz' + wx'y'z' + wx'yz + wxyz (4 product terms)
      x + w'y + wxy'z (3 product terms)
      x' + y + z (3 product terms)
  canonical sum or canonical SOP
    sum of minterms
    ex) for a 4 variables, w, x, y, and z
      w'xyz' + wx'y'z' + wx'yz + wxyz - canonical SOP
      x + w'y + wxy'z
      x' + y + z
  minimum sum of products
    one of those SOP expressions for a function that has the min # of product terms
    If more than one, minimum is the one with min # of literals (can have more than one)

## Slide 3
  sum term
    one or more literals connected by OR
    a+b'+c , b'
  standard sum term or maxterm
    a sum term that includes all the variables, either complemented or not
    for a 4 variables, w, x, y, and z
    w'+x+y+z’, w+x+y+z : maxterms
    x+y'+z : not maxterm but sum term
  product of sum (POS)
    one or more sum terms connected by AND
    ex)
      (w+x)(w+y) 2 sum terms
      w(z+y) 2 sum terms
      w 1 sum term
  canonical product or canonical POS
    product of maxterms